## Slide 1: 2DT901: Computer Organization Lecture 3
Lecture 3: Instruction sets, machine code and assembly code

## Slide 2: Instruction sets
Each microprocessor has an instruction set.
The instruction set is the set of all machine language instructions that the processor can execute, that is, the vocabulary of the processor.
The word machine code is used for the binary form of the instructions.
The book Patterson & Hennessy is based on the ARMv8 inststruction set, and most of the theory/examples is based on LEGv8.
LEGv8 is a simpler subset of ARMv8 and used for teaching.
LEG is a pun on the word ARM, and also a backronym for ”Lessen Extrinsic Garrulity”. See page 62 in the book!

## Slide 3: LEgv8 instructions
LEGv8 uses 32-bit instructions.
There are 32 registers, each register can store a 64-bit number.
An example of a LEGv8 instruction is: 10001011000001110000000011001000
Some of the bits are used to describe the instruction, some bits describe the parameters.
Exactly how many bits is used for each part depends on the type of instruction.
It is necessary to have a reference book/sheet to decode a machine instruction!

## Slide 4: Manual decoding
Let’s look closer at the instruction 10001011000001110000000011001000.
Look at the bits starting at the leftmost bit, identify the same pattern in the reference sheet.
Look in the table ”Opcodes in numerical order by opcode”
We find the pattern 10001011000 in the table, its mnemonic is ADD and its format is R
Now, look at the instruction format for R in the reference sheet.
The first 11 bits is the opcode, next 5 bits parameter Rm, and so on…. Divide the bits in the same pattern: 10001011000 00111 000000 00110 01000

## Slide 5: Interpreting the bits
In the beginning of the reference sheet, we see that the operation ADD is written R[Rd]=R[Rn]+R[Rm].
That is, in Assembly language, ADD Rd, Rn, Rm.
Rd is the destination register, Rn and Rm are the source registers.
For example, if Rd=1, Rn=2 and Rm=3 the assembly instruction is: ADD X3, X2, X1

## Slide 6: Final decoding
Look at the bit pattern again: 10001011000 00111 000000 00110 01000
  First 11 bits is instruction ADD
  Next 5 bits is Rm, 00111bin = 7dec
  Next 6 bits is shamt = shift amount. If all 0, it can be ignored.
  Next 5 bits is Rn, 00110bin = 6dec
  Last 5 bits is Rd, 01000 = 8dec
Conclusion: The Assembly instruction is: ADD X8, X6, X7

## Slide 7: Why decode instrcutions?
We rarely have to decode machine code manually today.
However, binary memory addresses often need to be handled by the programmer.
When debugging a program, it is sometimes important to understand binary and hexadecimal instructions and addresses.
Important to understand how many bits are used for different parts, for example it allows us to understand how many registers the computer can have.
It also gives an understanding of how large numbers can be given as parmeters to an instruction.

## Slide 8: Shifting binary numbers
An important concept when working with binary numbers is shifting.
Shifting right means that we insert a zero in the rightmost position and ”push” all bits to the left!
Shifting right is the opposite, works the same but in the other direction!
0 | 0 | 1 | 0 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0
Original number = 11dec
Shifted one step left = 22dec
1 | 0 | 1 | 1 | 0 | 0
Shifted two steps left = 44dec

## Slide 9: Result of shift
A shift left one step is the same as multiplying by 2
A shift left two steps is the same as multiplying by 4
And so on!
Conversely, a right shift one step is division by 2, right shift two steps is division by 4….

## Slide 10: Shifting and moving
The LEGv8 move instructions can also take a shift amount as a parameter.
This is given as a last parameter.
Example: MOVZ X1, #3, LSL 16
Inserts the decimal number 3dec=000000000000000000000011bin and then shifts the bits left 16 positions, gives the number 000000110000000000000000bin = 196608dec = 3*2^16
What is the purpose of this? Why not just insert the correct number from the beginning instead of shifting it to the right value?

## Slide 11: Inserting large numbers
The registers in LEGv8 are 64 bits and can handle very large numbers.
The MOVZ instruction takes an immediate value and inserts it into a register.
In the opcode, 16 bits are used to represent the immediate value.
With 16 bits, the largest possible number is 2^16=65 536
So, how can we insert a number such as 3 892 349?
The solution is to split the number and insert it in several parts.
This can be done in binary or hexadecimal form!

## Slide 12: Inserting a large number
Convert to hex: 3 892 349dec = 003B 647Dhex
Start by inserting the high 16 bits (the number 3B) into X0: MOVZ X0, #0x3B
Shift these bits 16 steps to the left, now we have 3B0000hex in register X0
Use the MOVK (move and keep) instruction to insert the lower 16 bits: MOVK X0, #0x647D
With the MOVK instruction, the existing higher bits are unchanged when new low bits are inserted!

## Slide 13: Memory access
To access data memory, the following LEGv8 instructions can be used:
  STUR: Store Unsigned Register
  LDUR: Load Unsigned Register
The instructions need a memory address as a parameter.
In LEGv8, the base address for the data memory is 0x10000000
The next address is 0x10000008. The distance between two memory addresses must be hexadecimal 8.

## Slide 14: Example: Memory access
MOVZ X7, #0x1000, LSL #16 MOVZ X1, #23 STUR X1, [X7] //Store content of X1 into memory address X7 MOVZ X1, #78 STUR X1, [X7, #8] //Store content of X1 into memory address one after X7
LDUR X2, [X7] //Store content of first memory address into X2 LDUR X3, [X7, #8] //Store content of second memory address into X2

## Slide 15: Loops and conditions
To create a conditional statement, there are some branch instructions in LEGv8.
The simplest are CBNZ (Conditional Branch if Not Zero) and CBZ (Conditional Branch if Zero).
CBNZ X1, label will jump to label if register X1 is not zero.
A label is a point in the code that a conditional statement can ”jump” to.

## Slide 16: A simple loop
MOVZ X1, #10 //Used as loop counter MOVZ X2, #1 loop: ADDI X2, X2, #2 SUBI X1, X1, #1 //Subtract 1 from loop counter CBNZ X1, loop //Branch if counter not 0

## Slide 17: Recommended reading
Patterson & Hennessy:
  Section 2.5: Representing instructions
  Section 2.6: Logical and shift operations
  Section 2.7: Selection and iteration (if-statements and loops)