## Slide 1: 2DT901: Computer Organization Lecture 5
Digital circuits
Karnaugh maps, adders and sequential circuits

## Slide 2: Simplification of digital circuits
A​ | B​ | C​ | Y​
0​ | 0​ | 0​ | 0​
0​ | 0​ | 1​ | 0​
0​ | 1​ | 0​ | 1​
0​ | 1​ | 1​ | 1​
1​ | 0​ | 0​ | 1​
1​ | 0​ | 1​ | 0​
1​ | 1​ | 0​ | 1​
1​ | 1​ | 1​ | 0​
From the previous lecture: Write a Boolean expression for the rows where output is 1
Y=A•B•C+A•B•C+A•B•C+A•B•C
A Karnaugh map is a truth table written as the picture below.
To simplify an expression, mark maximal groups of 1 that are powers of 2.
Write an expression for the groups of 1s
Y=A'B+AC'

## Slide 3: Karnaugh map with four inputs

## Slide 4: Karnaugh maps: Example 2

## Slide 5: Adder (addition circuit)
One of the most important parts of the ALU is the adder.
An adder calculates the sum of two binary numbers.
The first step is to build a 1-bit adder, that can add two one-bit numbers.
The result is one bit.
  0+0=0
  0+1=1
  1+0=1
  1+1=10 Here, the result is two bits. The left bit is ”overflow” or carry for next bit.

## Slide 6: Half adder and full adder
The half adder takes two 1-bit numbers and calculates the sum and carry.
Y=AB+A·B

## Slide 7: Full adder
To build an adder for more bits, the idea is to connect several 1-bit adders.
To make this work, an adder must be able to take a carry bit from another adder as input.
This type of adder is called a full adder.
The full adder can be connected in series to other full adders to build adders for longer binary numbers, for example, 8-bit adders, 16-bit adders, 32-bit adders, …

## Slide 8: Building a full adder

## Slide 9: A 4-bit adder
Here, four full adders are connected in series to form a 4-bit adder.
In exactly the same way, a number of Full Adders can be connected to make adders for binary numbers of any length!

## Slide 10: Combinational and sequential circuits
There are two different groups of digital circuits:
  Combinational circuits, where the output is completely determines by the input.
    For example: Adders, comparators
    In a combinational circuit, the output from a gate is not connected ”backwards” in a feedback loop.
  Sequential circuit, where the output is not only a function of the inputs, but also on what happened previously. This type of circuits is a type of memory that can save a state of the circuit.
    Example: Memory circuits, counters, shift registers
    A sequential circuit has a feedback loop.

## Slide 11: Example: SR latch
The SR latch stores an internal state, and is a type of 1-bit memory.
It can be constructed with a pair of NOR gate, as the picture shows.
Two inputs: S(Set), R(Reset)
Either Q or is 1, depending on state.
The SR latch has been given a special circuit symbol and is available as an IC circuit.
In lab assignment 2, you will investigate the behaviour of this circuit!

## Slide 12: Recommanded reading and videos
Karnaugh maps and simplification of logic expressions: https://www.youtube.com/watch?v=RO5alU6PpSU https://www.youtube.com/watch?v=J71fceNlGAY
Adders: Patterson&Hennessy, Appendix A.5 https://www.youtube.com/watch?v=ecn-8iGDRSo
Secuential circuits and memory elements: Patterson&Hennessy, Appendix A.8 https://www.youtube.com/watch?v=L5V1IxFhq0k